Experimental results -
elemental cross section
Yield obtained from run 4306 taken in GSI 2021 campaign
Fiducial cross section (θ<2.5°) to limit overall noise
➔ high consistency
9
Giacomo Ubaldi

---
Experimental angular differential
cross section
z=4
z=1
z=2
z=3
z=5
z=6
z=7

---
Experimental data issues
GLB tracking
4 points (VT) + 1 (TW)
High inefficiency in track
reconstruction
Is it a problem of VT?

---
Global vs VT theta
VT theta
Global theta
It seems tracks with wider angle aperture than 2/3° are not reconstructed

---
VT synch
correlazione tracce bm-vtx per eventi fino a 60 k
correlazione tracce bm-vtx per eventi da 60k a 65k
→ events up to 65000 are synchronized

---
VT – TW allignment (fragments)
TW points (global frame)
Projection of the tracklet in
the global frame
→ TW is shifted wrt to VT

---
VT – TW allignment (beam)
TW points (global frame)
Projection of the tracklet in
the global frame
→ TW is shifted wrt to VT

---
Tracklets Phi distribution
oxygen
frags
Azimutal distribution peaked around 18° → is the VT tilted?

---
Vectorial sum of all the tracklets of all events
Global frame:
fragment VT direction:	theta = 1.123522	phi = 29.527197
beam VT direction:	theta = 1.102172	phi = 25.031881
VT local frame:
fragment VT direction:	theta = 0.361786	phi = 29.527197
beam VT direction:	theta = 0.354997	phi = 25.031881
→ VT is rotated of ~1°
    193 cm * tan(1°) ~ 4 cm → TW is shifted of 4 cm wrt to VT

---
Migration Matrix studies – TW points
Ztrue
Ztrue
Zreco
Zreco
TW points born in TG
All TW points

---
MC TW points
/gpfs_data/local/foot/Simulation/GSI2021_MC/16O_C_400_2_shoereg.root
ID > -1

---
Migration Matrix studies – TW ALL POINTS
Ztrue
Zreco
All TW points
Tail of H and He

---
Migration Matrix studies – TW ONLY FRAGMENTS
Ztrue
Zreco
Fragments from target

---
Migration Matrix studies – TW ONLY FRAGMENTS
Ztrue
Zreco
Fragments from target

---
Migration Matrix studies – TW ONLY FRAGMENTS
Ztrue
Zreco
Secondary fragments

---
Migration Matrix studies – TW vs Global Tracking
Ztrue
Ztrue
Zreco
Zreco
All TW points
All reco tracks

---
Migration Matrix studies – Global Tracking
Ztrue
Zreco
All reco tracks
Reco tracks after trigger simulation

---
Run 4306
gpfs_data/local/foot/DataGSI2021/data_test.00004306.physics_foot.daq.RAW._lb0000._FOOT-RCD._0001.data

---
Phi distribution of ORIGIN of tracklets

---
MC Phi distribution of ORIGIN of tracklets