## Slide 1
PhD purpose
Giacomo Ubaldi
Giacomo Ubaldi
1
Notes: OK in this presentation i want to speak about in vivo monitoring of the dose or of the range in add on therapy what it is about the main methods and research and the first clinical
<numero>

## Slide 2
1
depth- dose profile for X-rays and charged particles as a beam
Hadrontherapy vs radiotherapy:
Finite range
Localized dose profile
Nuclear fragmentation
tumor
Hadrontherapy
Sketch of a treatment planning system on brain-located tumor
Notes: Let's start from the beginning. Radiation therapy represents a way to exploit an external beam of radiation, which delivers energy, or those in a specific region of the human body where there is a tumour in order. To kill the tumour cells, or to limit their proliferation. He, according to the kind of radiation in the beam, the delivery of those is different. Let's consider now the dozer profile. So there is of those in terms of depth in the human body and what are the main differences between radiation therapy. Radiotherapy, the most common one which exploits the X rays and add on therapy. The most promising one which uses charged particles. What we can see is that for add on therapy we have a highest physical selectivity, which means that the highest release of those is a focused in a very specific region. Very close to the range. A end of the charged particle and it is called Brad Pick. So according to the energy given to the BMA, it is possible to have a black pika in the specific region of the tumour. We can say. So add on therapy. Can be two favourable with reference to radiotherapy becausr it's hayastan steepest gradient of those releasing just a region makes the highest spare of entity issues before and after the two rural region. However there are also some limits to the best. Then potentiality of this technique, and they are the range uncertainties in the clinical application of my treatment. So after his planning, it is possible that there are some discrepancy in the range of my beam. There can be shift which means. Chiefs of the black Beak in the entity in the tissues of the human body. In particular, there would be another dozing of tissues after the tumour and then under dozing in the two rural region. The consequence of this are that it is possible. to even create damages of arctic issues more than one than the ones of
<numero>

## Slide 3
Nuclear Fragmentation
1
Sketch of Nuclear fragmentation
Proton beam:
Carbon beam:
~ 200 MeV
~ 400 MeV/u
Damage in all the path
Damage after the BP

## Slide 4
Space radioprotection
1

## Slide 5
Space radioprotection
1
SOLAR RADIATION
suddenly
92% p
6% He
2% HZE
E<1 GeV/n

## Slide 6
Space radioprotection
1
COSMIC RAYS
constantly
90% p
9% He
1% HZE
0.001 < E < 1014 GeV/n

## Slide 7
Space radioprotection
1
MARS

## Slide 8
Space radioprotection
1
MARS
fragmentation
Effects on:
Space craft hull and structure
Shielding
Astronaut’s body

## Slide 9
Space radioprotection
1
MARS
Fluence
Dose
Dose equivalent
fragmentation

## Slide 10
The FOOT experiment
1
FOOT (FragmentatiOn Of Target)
measure double differential cross sections in angle and kinetic energy with a maximum uncertainty of 5%
Energies between 200 MeV/u and 700 MeV/u for hadrontherapy and space radioprotection applications
isotopic identification by measuring all kinematic quantities
table top setup to be moved according to beam availability

## Slide 11
The FOOT detector
1
BEAM
z

## Slide 12
The FOOT detector
<numero>
Pre-target region
Start
Counter
Beam
monitor
Target
BEAM
z

## Slide 13
The FOOT detector
<numero>
Tracking region
Target
Vertex
Tracker
Inner
Tracker
Microstrip Silicon
Detector
Permament
Magnets
BEAM
z

## Slide 14
The FOOT detector
<numero>
Downstream region
ToF Wall
Calorimeter
BEAM
z

## Slide 15
The FOOT detector
<numero>
Pre-target region
Tracking region
Downstream region
Start
Counter
Beam
monitor
Target
Vertex
Tracker
Inner
Tracker
Microstrip Silicon
Detector
Permament
Magnets
ToF Wall
Calorimeter
BEAM
z

## Slide 16
GSI 2021 analysis
<numero>
Analysis on MC and real Data of 16O 400 MeV/u on 5 mm C target
taken at GSI (Dollmstadt) in 2021
Partial setup:
No B field → no p information, so no mass reconstruction possible
Only one matrix of calorimeter → limited kinetic energy information
First preliminary goal: charge changing angular differential cross section
SC
BM
TG
VTX
MSD
TW
CALO

## Slide 17
Differential Cross section
<numero>

## Slide 18
Differential Cross section
<numero>
N° of primary
events
N° of scattered
centers

## Slide 19
Differential Cross section
<numero>
N° of primary
events
N° of scattered
centers
Phase space

## Slide 20
Differential Cross section
<numero>
N° of primary
events
N° of scattered
centers
Phase space
efficiency

## Slide 21
Differential Cross section
<numero>
N° of primary
events
N° of scattered
centers
Phase space
efficiency
Yield of all fragments

## Slide 22
Fragments identification
<numero>
From Bethe – Bloch formula I can get z:
Infos taken from SC and TW
Histo con z interi,
Perché il TW usa algo specifico
z=8
z=7
z=6
z=5
z=4
z=3
z=2
z=1
dE
ToF

## Slide 23
Track reconstruction
<numero>
Kalman Filter reconstruction of a track
Start from VT tracklets
Projection to possible planes of IT
KF extrapolation to MSD
KF extrapolation to TW
Fit the track candidates and extract reconstructed quantities: Z, momentum ...
TW
MSD
VT
Simulation of track reconstruction on GSI 2021 data
No B field present

## Slide 24
Isotopes identification
<numero>
Mass reconstruction using all FOOT subdetectors:
In our data no tracker and calorimeter → mass measurement only in MC data!
Augmented Lagrangian Method
Aχ 2 = 11.66 ± 0.38
risoluz. 3.2 %
χ 2 < 5

## Slide 25
Pile-up removal
<numero>
What it was seen in the last data taking (GSI - CNAO 2021) is that the beam flux is not constant → pile-up events
Pileup projectile
Single projectile
constant
threshold
discrimination
method
2 crosses
4 crosses
4 crosses
pileup projectile: >4 crosses
Single projectile: 4 crosses
2 crosses

## Slide 26
Pile-up removal
<numero>
DataGSI2021/data_test.00004310.physics_foot.daq.RAW._lb0000._FOOT-RCD._0001.data
Both minimum bias trigger and trigger fragmentation
Charge
t(ns)
PileUp on 600.000 events ~ 1%

## Slide 27
Bibliography:
Review:
Proton thepary physics, cap 16 (In Vivo Dose Verification - Katia Parodi )
In vivo proton range verification: a review, Antje-Christin Knopf and Antony Lomax 2013
In vivo range verification in particle therapy - Katia Parodi
In-vivo PET:
Online Irradiation Control by Means of PET, Chapter 31- Fine Fiedler, Daniela Kunath
The INSIDE Project: Innovative Solutions for In-Beam Dosimetry in Hadrontherapy, Marafini, Battistoni
Detection of Interfractional Morphological Changes in Proton Therapy: A Simulation and In Vivo Study With the INSIDE In-Beam PET
Prompt gamma monitoring:
First clinical application of a prompt gamma based in vivo proton range verification system, Christian Richter
Charged particles monitoring:
Design of a new tracking device for on-line beam range monitor in carbon therapy, Traini
Inter‑fractional monitoring of 12 C ions treatments: results from a clinical trial at the CNAO facility, Fischetti

## Slide 28
Back up slides
<numero>

## Slide 29
Kalman filter in pills
<numero>
1. Take an ideal particle in vacuum. If we
add air + detector layers, trajectory
changes due to M.S. and energy loss.
2. We’ll see some measurement hits on
the detector layers (considering finite
detector uncertainty).
Filtering
3. Propagate the first hit to the next
layer. Propagator Matrix F.
4. Find the best compromise between
the propagated point and the closest
hit on the 2 nd layer. Use a Chi2 and a
Projection Matrix H.
5. Iterate 3 and 4 for the next layers.

## Slide 32
<numero>
Sharp gradient risks:
undershooting tumor
overdosing normal tissues
Exponential attenuation risks:
little smear of the dose
+ range
uncertainties
Effects of range uncertainties
dose
depth
depth
 effects on proton
treatments
tumor
tumor
tumor
Notes: <numero>

## Slide 33
Beam specifications
<numero>
Specification of SOBP charged partice and X-ray depth–dose distribution in longitudinal size
Ds
Dmax
Dexit
Sharp gradient risks:
undershooting tumor
overdosing normal tissues
Exponential attenuation risks:
little smear of the dose
dose
depth
Depth – dose distribution with range uncertainties
dose
depth
+ range
uncertainties
Notes: <numero>

## Slide 34
An example: prostate cancer
<numero>
Safety margins ~ 4 mm
not possible to apply the optimal treatment
  Patched beams
Planning treatment with conformal RT
Planning treatment with PT – Patched Beams
Planning treatment with PT – One Beam
Example of Patched Beams application
Every mm is important
Must know and limit uncertainties
Due to
too high
range
uncertainties

## Slide 35
Sources of uncertainties
<numero>
Multiple scattering
Physics related:
Range straggling
Formation of clinical proton beam
(random uncertainties)
Range straggling
Multiple scattering of the beam with absorbers

## Slide 36
Sources of uncertainties
<numero>
CT of face layer, presence of metal implants in the mouth
CT related:
Inaccurate Unit conversion
Presence of artifacts
(systematic uncertainties)
Fundamental for the
treatment planning
Sketch of a CT machine

## Slide 37
Sources of uncertainties
<numero>
CT of lung, at the beginning of the treatment and after 5 weeks:
Tumor anatomy changes
Patient related:
patient position
density dishomogeneities
organ motions
anatomy changes
(random/systematic uncertainties)
A proton beam in water crosses a material with higher density: this changes drastically the range
p

## Slide 38
In vivo range verification
<numero>
irradiation
time
Pre-treatment Ion beams radiography
In - treatment PET
Prompt gamma detection
Charged particles detection
Implantable dosimeters
After treatment In-room / Offline PET
After therapy MRI
On-time feed-back
exploit the treatment beam
Clinical tests

## Slide 39
Diagnostic vs In vivo range verification
<numero>
Exploit activity of radionuclides
Recostruction of the biological functions of organs via images / measurements
Exploit activity of secondary fragments of treatment beams
Reconstruction of the release of dose of the beam via measurements/ images
 «teragnostic»
Diagnostic PET and SPECT
In-vivo monitoring PET and SPECT machine
In the best scenario, it is possible to use the same machines

## Slide 40
PET machines
<numero>
Sketch of PET working principle
Example of diagnostic PET machine
and in-beam PET machine (the latter at GSI)
Full cyrcle vs double-head system
Higher gamma ray background
No additional dose costs for the patient

## Slide 41
In-beam vs off-line PET machines
<numero>
In beam:
2 head cottected to the treatment accelerator
no repositioning of the patient
on-line corrections of the treatment would be possible
It compromises patient throughput.
Low angle acceptance
Low metabolic washout
Off – line:
Full ring scanners offer a higher detection efficiency CT scanner (PET-CT) compensating for the unavoidable patient movement
Low statistics because low activity after some minutes
Higher metabolig washout
In room:
directly following treatment delivery
using the same patient immobilization and treatment couch.

## Slide 42
in-beam PET purposes
<numero>
Able to detect:
range of the ions in vivo
unexpected density modifications
inaccuracies in patient positioning
Prediction of beta+ activity vs. in-beam PET measurement. The measurement indicated a
slight rotation of the patient counterclockwise
Anatomical changes, their effects on dose and the approximate quantification of dose
deviations from the treatment plan.

## Slide 43
in-beam PET constraints
<numero>
Constraints:
restricted knowledge about the elemental composition metabolic washout
low resolution due to spatial limitations
Low statistics, no quantitavie measurements
High background (gamma prompt, neutrons due to passive scattering beams..)
Expencive
Further researches:
Tof, new detectors, highest graphic algoritms, highest efficiency photons, hypofractionation
treatments with higher dose delivery, improved imaging detection

## Slide 44
PGs detectors
<numero>
slit gamma camera
1-D profile
slit against bkg
fast scintillator detector
dE/dx + TOF from scint
used for discrimination
Compton camera
define origin cone from CC
electron tracking Compton camera
TPC + scint
TPC: angular localization
Less CC but highest efficiency
35 s
35 s

## Slide 45
PGs vs β+ gammas
<numero>
no physiological washout
no delay detection
higher yield
reduced signal attenuation
better resolution
Pro:
much higher SNR
Cons:
Needed high detection efficiency good spatial and time resolution
Schematic drawing of the 3-γ imaging principle On- and off-line monitoring of ion beam treatment, Katia Parodi
Full ring PET + TPC Compton camera:
new concept of Hybrid detector systems

## Slide 46
emission distribution properties
<numero>
Detector: Single Proton interaction vertex imaging
(Drift chambers,
Inorganic crystals)
 Seconday particle emission point reconstruction:
Primay beam direction by beam delivery system
Particle vertex direction by tracker
Optimal angle detection:
Low angle
Higher kinetic energies of particles
Higher flux
Lower MS
High angle (~ 90°)
Better spatial resolution
Higher efficiency: no bkg
Spatial uncertainties due to angle emission
Sketch of single proton IVI
Back-tracking
trade off, generally ~ 60°
Particle composition:
Mainly p,d,t,
energy vs. time of flight (expressed in nanoseconds) distributions
C beam
300 Mev/U
H20 target
α = 30°
d = 2.2 m