Analysis Studies for GSI2021 campaign
7/09/2022
Giacomo Ubaldi

---
Goal
Analysis of data taken at GSI in 2021 of 16O 400 MeV/u and 200 MeV/u against C as target
Analysis integrated in SHOE and optimization for specific data
TW
MSD
BM
VTX
SC
CALO
TG
Specific goal:
Elemental fragmentation cross section
Angular differential cross section:

---
Reconstruction
Starting with MC data reconstructing fragment charge
Study of the MC tracks reconstructed by tracking algo
Migration Matrix diagonal + misreconstruction
Zreco
Mis-reconstruction around 1% for every charge
Main contribution of misreconstructed charge
for Z=8 and Z=1,2 → where the statistics is high
Ztrue

---
Reconstruction
Starting with MC data reconstructing fragment charge
Study of the MC tracks reconstructed by tracking algo
Migration Matrix diagonal + misreconstruction
Zreco
Mis-reconstruction around 1% for every charge
Main contribution of misreconstructed charge
for Z=8 and Z=1,2 → where the statistics is high
First approximation → cut Ztrue = 8 (simulation
of triggered dataset)
Ztrue

---
Reconstruction, cuts
TW
MSD
BM
VTX
SC
CALO
TG
Cuts can be applied in order to make the migrant matrix more diagonal
Let’s inspect how charge is reconstructed in TW

---
Reconstruction, Track Algo
One source of systematics could be the presence of Pile up / Ghost hits in the TW point of the track
twp→GetMcTracksN() > 1 :
The object TATWPoint is the superimposition
of the Hitx and Hity on the rispective bars
It is possible that every bar is hitted with more than
a particle at the same time:
Pile up
Ghost hits
The reconstructed charge is then wrong because of
a wrong hits input
→ remove them asking GetMcTracksN() == 1

---
Reconstruction, Track Algo
Applying the TW Ghost Hits cut:
After cut:
Zreco
Zreco
Ztrue
Ztrue
Es Z=6
Mis-reconstructed: 2.7%
mis-reconstructed: 3%
TW ghost impact to be considered as a systematics/bkg

---
Reconstruction
TW ghost impact to be considered as a systematics/bkg

---
Reconstruction, Yield
Y(Z)
Zreco
TW ghost impact to be considered as a systematics/bkg

---
Reconstruction, efficiency
Reconstruction efficiency
reco tracks / simulated particles

---
Elemental fragmentation cross section
Values of Z=1,2 depends
on the cut MC (es. angular acceptance)
Z

---
Angular differential cross section
Es Z=6
Track efficiency
Theta (°)
mbarn / degree°

---
Angular differential cross section

---
Conclusions
First preliminary results based on MC events with a reasonable order of magnitude
To do:
Study of further efficiency and systematics due to TW and Track algorithm
Background to be considered: es fragmentation after target
Improve the simulation of trigger
Apply cross section “recipe” to real data

---
Reconstruction, TW Algo
Let’s study the MC particle, directly generated by the simulation
MC particles generated in TARGET which fragment after the TW → what can be detected by my apparatus
ZMC vs ZTW-ALGO
ZTW
Much more diagonal
TW algo systematic is not the main problem
Ztrue

---
Reconstruction, efficiencies
9% of Z=7 are false
BKG subtraction?
After TW filter
Zreco
Ztrue

---
Reconstruction, Track Algo
Another source of systematics can be the way points are collected in a track
In the best scenario, all points belong to the same particle:
Reconstructed track:
x
x
x
x
x
x
x
x

---
Reconstruction, Track Algo
However, due to the presence of a lot of secondary fragmentation, some points can belong to other particles.
Reconstructed track:
x
x
x
x
x
x
x
x
Wrong points collected in the track
The McId of the track is given by the most present particle in the collection
However, if the TWPoint is of another particle → its McId is different
→ filter out all the tracks in which McIdtrack ≠ McIdTWPoint

---
Reconstruction, Track Algo
Applying the Id filter filter:
After filter:
Zreco
Zreco
Ztrue
Ztrue
Incidenza wrong points = 0.7%
Wrong point to be considered as a systematics
Incidenza TW (ghost + wrong points) = 2 %

---
Reconstruction, efficiencies
Reconstruction efficiency
reco tracks / simulated particles
After TW filter
Before TW filter

---
Reconstruction, efficiencies
9% of Z=7 are false
BKG subtraction?
After TW filter
Zreco
Ztrue

---
Global reconstruction
Global reconstruction of an event
Particle ID: Z,A
Kinematics: E,p
Angular distribution: θ
From SHOE branch “glbreco_v1”:
libs/src/TAGfoot/GlobalRecoAna.cxx
.root file with histograms of
variable distribution
Aim of the new software:
Measure differential cross section σ (Z,A,θ,E)
wrt all combination of variables
Written in python
G. Ubaldi

---
Z
Exampe of
Input file
From SHOE
θ
There are only histos of A
Every subdirectory is due to
input binning of the variable
Every histo is univocally discriminated
by its path
E
A
The software
takes info dinamically about input
variables and binning
Generates differential distribution
wrt all combinations of variables
G. Ubaldi

---
Output directories

---
https://baltig.infn.it/gubaldi/xshoe
G. Ubaldi